## Slide 1: Barcelona Supercomputing Center The Future HPC will be Open
Prof. Mateo Valero
December 14, 2020

## Slide 2: Barcelona Supercomputing Center Centro Nacional de Supercomputación
Spanish Government 60%
Catalan Government 30%
Univ. Politècnica de Catalunya (UPC) 10%
BSC-CNS is
a consortium
that includes
BSC-CNS objectives
Supercomputing services
to Spanish and EU researchers
R&D in Computer, Life, Earth and
Engineering Sciences
PhD programme, technology transfer, public engagement

## Slide 3: People evolution
BSC Staff evolution 2005 - 2020
August 31, 2020
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Total | 65 | 114 | 164 | 229 | 279 | 302 | 310 | 321 | 358 | 433 | 447 | 475 | 529 | 613 | 668 | 693
Notes: 87

## Slide 4
MareNostrum 4
Total peak performance: 13.9 Pflops
General Purpose Cluster: 11.15 Pflops (1-07-2017)
CTE1-P9+Volta: 1.57 Pflops (1-03-2018)
CTE2-Arm V8: 0.65 Pflops (12-2019)
CTE3-AMD: 0.52 Pflops (12-2019)
MareNostrum 1
2004 – 42.3 Tflops
1st Europe / 4th World
New technologies
MareNostrum 2
2006 – 94.2 Tflops
1st Europe / 5th World
New technologies
MareNostrum 3
2012 – 1.1 Pflops
12th Europe / 36th World
MareNostrum 4
2017 – 11.1 Pflops
2nd Europe / 13th World
New technologies

## Slide 5: Today´s technology trends
Massive penetration of Open Source Software
  IoT (Arduino),
  Mobile (Android),
  Enterprise (Linux),
  HPC (Linux, OpenMP, etc.)
New Open Source Hardware Momentum from IoT and the Edge to HPC
  RISC-V
  OpenPOWER
  MIPS
Moore´s Law + Power = Specialization (HW/SW Co-Design)
  More cost effective
  More performant
  Less Power

## Slide 6: Linux History
1991: Started development, release
1992: X Windows released
1998: Adopted by many major companies
2004: BSC Supercomputer OS
2009: Basis for many new business systems and the cloud
2013: Android in 75% of the world smart phones
2015: De facto OS for IoT, mobile, cloud, and supercomputers

## Slide 7: HPC Today
Europe has led the way in defining a common open HPC software ecosystem
Linux is the de facto standard OS despite proprietary alternatives
Software landscape from Cloud to IoT already enjoys the benefit of open source
Open source provides:
  A common platform, specification and interface
  Accelerates building new functionality by leveraging existing components
  Lowers the entry barrier for others to contribute new components
  Crowd-sources solutions for small and larger problems
What about Hardware and in particular, the CPU?
CPUs/GPUs/ASICs
HW Systems
OS
Compiler/Toolchain
Schedulers
Libraries/Platforms
Applications
OPEN
CLOSED
Linux
LLVM
COMPS
OpenMP
GROMACS,NAMD, WRF, VASP, etc.
OCP

## Slide 8: Mont-Blanc HPC Stack for ARM
Industrial applications
System software
Hardware
Applications

## Slide 9: The Exascale Race – The Japanese example

## Slide 10: The Exascale Race – The Japanese example

## Slide 11: The European Open System Stack
TRL 8-9
TRL 5-7
TRL 3-4
TRL 1-2
Notes: Blue (TRL 8-9) Mature European technology products that are on-par internationally or even enjoy supremacy
Green (TRL 5-7) European technology with core European industrial support less than 2-3 years (short term) away from product maturity
Yellow (TRL 3-4) European technology with a 5-year roadmap (medium term) to become a competitive product, supported by industrial partners, with potentially suitable core competences
Red (TRL 0-2) Technology with low European capability and a >7-year (long term) roadmap toward a competitive product offering with no or very few mature industrial partners

## Slide 12: Why Europe needs its own processor
Processors now control almost every aspect of our lives
Security (back doors, etc.)
Possible future restrictions on exports to EU due to increasing protectionism
A competitive EU supply chain for HPC technologies will create jobs and growth in Europe

## Slide 13: RISC-V History
2010: Started development and initial proposal
2015: RISC-V Foundation formed
2019: Adopted by many major companies
  Starting in the embedded market with already over 1 Billion CPUs
2020
  RISC-V Foundation moves to Switzerland
The time is now to embrace and support RISC-V from IoT to HPC

## Slide 14: RISC-V is democratizing chip-design
Google
Amazon
Western Digital
More and more global IT actors are adopting RISC-V architectures to be vendor independent
And of course the entire IoT ecosystem for lower performance, lower energy applications.
Major opportunity for ICT industry also in Spain
Alibaba

## Slide 15: HPC Tomorrow
Europe can lead the way to a completely open SW/HW stack for the world
RISC-V provides the open source hardware alternative to dominating proprietary non-EU solutions
Europe can achieve complete technology independence with these foundational building blocks
Currently at the same early stage in HW as we were with SW when Linux was adopted many years ago
RISC-V can unify, focus, and build a new microelectronics industry in Europe.
CPUs/GPUs/ASICs
HW Systems
OS
Compiler/Toolchain
Schedulers
Libraries/Platforms
Applications
OPEN
Linux
LLVM
COMPS
OpenMP
GROMACS,NAMD, WRF, VASP, etc.
OCP
RISC-V, OpenPower, MIPS

## Slide 16: Open Source Beyond 2020
“Open Source has become mainstream across all sectors of the software industry during the past 10 years. To a large extent, open software re-use has proven economically efficient. The level of maturity of Open Source Hardware (OSH) remains far lower than that of Open Source Software (OSS). However, business ecosystems for OSH are developing fast so that OSH could constitute a cornerstone of the future Internet of Things (IoT) and the future of computing.”
- DG Connect & DG IT Workshop, Brussels, Nov. 14-15, 2019
Source: https://ec.europa.eu/digital-single-market/en/news/workshop-about-future-open-source-software-and-open-source-hardware

## Slide 17: From IoT, Edge Computing, Clouds to Supercomputers

## Slide 18: Current BSC RISC-V European Accelerator & CPU Landscape
Open Source HW
MEEP
Open Source SW
Exploitation
European Open Source Ecosystem
Arm GPP EuroHPC-2020-01 subtopic A
RISC-V Accelerators
RISC-V CPUs
eProcessor
EPI - SGA2
The European PILOT (RISC-V)
Note: Collaboration between all RISC-V projects possible
EPI - SGA1

## Slide 19: Rebuilding the European CPU Industry
EPI
MEEP
eProcessor
IP/Infra
IP/Infra
Design
Closed + Open
Open
Research
Production
eProcessor
EPI RISC-V PILOT
Exascale
IP/Infra
IP/Infra
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 826647
Notes: EPI Phase 1: EPAC RISC-V accelerators: Vector, ML/Stencil, Variable Precision, + shared cache coherent L2, and NoC. Shared Arm infrastructure
MEEP: FPGA emulation platform. ACME Accelerated Compute and Memory Engine: RISC-V accelerator w/ Vector processor + Video and neural network coprocessors.
eProcessor: 2-way OOO RISC-V processor, single core and dual core implementation (tapeout), coherent caches and off-chip coherent link, bioinformatics accelerator
EPI RISC-V Pilot: The European PILOT: Pilot using Local and Open Technologies: 2 All-European IP, independent PCIe 6.0 w/ CXL 3.0 accelerator chiplets, Vector and ML/Stencil (VEC and MLS). Open Compute Platform Infrastructure. Liquid Immersion cooling. Full RISC-V SW stack from GROMACS and EC-EARTH on the VEC side to Video Anomaly Detection, NLP and Machine Learning on the MLS side. Joint HPC +HPDA appt.

## Slide 20: The European Processor Initiative
In the same way BSC led the development of ARM processors for HPC in the various MontBlanc projects, now it leads the RISC-V HPC accelerator development in EPI
EPI is a 100% funded EuroHPC project (120 M€ ) to develop European processor technology by 2022
BSC was the original initiator of EPI and most active proponent in the scientific and technical community
EPI is led by Atos/Bull with 27 partners from leading HPC industrial and academic centres

## Slide 21: EPI Partners
Notes: 3 new partners
Embedded FPGA Embedded Security, and especially Secure OS
HW/SW co-design under automotive Functional Safety conditions
Soon a 4th one

## Slide 22: EPAC architecture
Main Contributors:
RISC-V in the Tile: 8 Vector cores, 8 STX, 1 VRP
Vector Core :
  Spain + Italy + Croatia
  C: RISC-V Scalar core
  V: RISC-V Vector core: 8 lanes
STX
  Switzerland + Germany
  RISC-V NTX (AI/ML/DL) + Stencil
VRP
  France
  RISCV + Extended precision FPU
GPP world/ ARM
Bridge
RNI
RNI
noc
L2
HN
HNF
L2
HN
HNF
L2
HN
HNF
RNF
AXI Lite
Peripherals
Peripherals
Peripherals
C
V
STX
RNF
C
V
STX
Bridge
RNI
RNI
VRP
CEA
Chalmers
FORTH
Semidynamics
BSC
ETH + FhG
EXTOLL
ETH
Objective: Develop & demonstrate fully European processor IPs based on the RISC-V ISA. Build on existing EU IP, leverage EU background and vision
Provide a very low power and high computing throughput accelerator for HPC & Emerging -> Automotive
IST
UNIBO

## Slide 23: Rebuilding the European CPU Industry
EPI
MEEP
eProcessor
IP/Infra
IP/Infra
Design
Closed + Open
Open
Research
Production
eProcessor
EPI RISC-V PILOT
Exascale
IP/Infra
IP/Infra
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 826647
Notes: EPI Phase 1: EPAC RISC-V accelerators: Vector, ML/Stencil, Variable Precision, + shared cache coherent L2, and NoC. Shared Arm infrastructure
MEEP: FPGA emulation platform. ACME Accelerated Compute and Memory Engine: RISC-V accelerator w/ Vector processor + Video and neural network coprocessors.
eProcessor: 2-way OOO RISC-V processor, single core and dual core implementation (tapeout), coherent caches and off-chip coherent link, bioinformatics accelerator
EPI RISC-V Pilot: The European PILOT: Pilot using Local and Open Technologies: 2 All-European IP, independent PCIe 6.0 w/ CXL 3.0 accelerator chiplets, Vector and ML/Stencil (VEC and MLS). Open Compute Platform Infrastructure. Liquid Immersion cooling. Full RISC-V SW stack from GROMACS and EC-EARTH on the VEC side to Video Anomaly Detection, NLP and Machine Learning on the MLS side. Joint HPC +HPDA appt.

## Slide 24: MareNostrum 5. A European pre-exascale supercomputer
200 Petaflops peak performance (200 x 1015)
Experimental platform to create supercomputing technologies “made in Europe”
217 M€ of investment
Hosting Consortium:
Spain
Portugal
Turkey
Croatia
The acquisition and operation of the EuroHPC supercomputer is funded jointly by the EuroHPC Joint Undertaking, through the European Union’s Connecting Europe Facility and the Horizon 2020 research and innovation programme, as well as the Participating States Spain, Portugal, Croatia, and Turkey

## Slide 25: MEEP: MareNostrum Experiment Exascale Platform
MEEP is a flexible FPGA-based emulation platform that will explore hardware/software co-designs for Exascale Supercomputers and other hardware targets, based on European-developed IP. The project provides two functions:
  An evaluation platform of pre-silicon IP and ideas, at speed and scale.
  A software development and experimentation platform to enable software readiness for new hardware.
MEEP will enable software development, accelerating software maturity, compared to the limitations of software simulation. IP can be tested and validated before moving to silicon, saving time and money.
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
Notes: Open Source ISA
  RISC-V
Exascale system at less than 30 MW
  Reduce the Host CPU tax
  Reduce/remove data copying/movement
Support traditional HPC & emerging HPDA (AI/ML/DL)
Accelerate Dense and Sparse workloads
What can be built by industry in 5 years
  Host agnostic: Supports ARM, x86, Power and RISC-V
  Targeting 5 nm or better, 150 mm sq chiplet
  What will we demonstrate in the FPGA
Self-hosted accelerator
  No data movement between host and accelerator
Map to a multi-FPGA+HBM emulation platform

## Slide 26: Accelerated Compute and Memory Engine (ACME) Architecture
VAS Tile
JTLB
MCPU
RB
HBI
DB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
MCPU
RB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
DB
DB
DB
DB
DB
DB
DB
HBI
HBI
HBI
HBI
HBI
HBI
HBI
JTLB
MCPU
RB
DB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
MCPU
RB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
DB
DB
DB
DB
DB
DB
DB
HBI
HBI
HBI
HBI
HBI
HBI
HBI
HBI
SerDes
JTLB
JTLB
SerDes
SerDes
SerDes
SerDes
SerDes
SerDes
SerDes
DFx
HBM3+
NVRAM
HBM3,+
NVRAM
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
L2 I$
DFx
L2 I$
DFx
L2 I$
DFx
L2 I$
VAS Tile
XP
Core0
Core1
Core2
Core3
Core4
Core5
Core6
Core7
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
Core
Scalar Core
CGMT
16 Fused Lane VPU
Systolic Shell
Systolic Arrays
Shared L2
Notes: Disaggregated Architecture.
Move Memory related compute to the Memory Controller, Memory Contoller CPUs: Process Vector memory requests, especially scatter/gather. Can look into the future.
Use the L3 Cache as a DRAM row buffer cache for virtual, memory interleaving. Leverage the future memory request knowledge to save future DRAM requests to on-chip memory
Assumes we have a limited capability scratchpad to store vectors (stride-1 data) as virtual register info for latter use, DMA/stream into the physical register file. Can make registers longer or add more registers (renaming).
VAS (Vector and Systolic array) Tile: Shared L2, (coherent), private L1$’s, 8 cores with each core containing 8-16 VPUs. VPUs can be split into groups of 2 lanes or phase into a group of 8/16 lanes. Groups are mapped to threads. Many small threads for sparse and 1 thread for dense. Vector length dependent along with the type of parallelism to extract, DLP/TLP, etc.
Assuming Jumb page TLB (1 GB pages, can have large pages (2 MB)).
Shared L2 Instruction cache
Assuming HBM3+ with stacked NVRAM 16/128 GB/chiplet, 8 chiplets/module plus an I/O chiplet
Assuming Mesh NoC between tiles.
PCIe to talk to hosts
3 or more Accelerator-to-accelerator interfaces to scale the number of coherent accelerators.

## Slide 27: Mapping ACME Architecture to an FPGA
LINUX
IoT to HPC, AI/ML/DL
VAS Tile
JTLB
MCPU
RB
HBI
DB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
MCPU
RB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
DB
DB
DB
DB
DB
DB
DB
HBI
HBI
HBI
HBI
HBI
HBI
HBI
JTLB
MCPU
RB
DB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
MCPU
RB
MCPU
RB
MC
MC
MCPU
MCPU
RB
RB
MC
MC
DB
DB
DB
DB
DB
DB
DB
HBI
HBI
HBI
HBI
HBI
HBI
HBI
HBI
SerDes
JTLB
JTLB
SerDes
SerDes
SerDes
SerDes
SerDes
SerDes
SerDes
DFx
HBM3+
NVRAM
HBM3,+
NVRAM
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
VAS Tile
L2 I$
DFx
L2 I$
DFx
L2 I$
DFx
L2 I$

## Slide 28: Rebuilding the European CPU Industry
EPI
MEEP
eProcessor
IP/Infra
IP/Infra
Design
Closed + Open
Open
Research
Production
IP/Infra
IP/Infra
eProcessor
EPI RISC-V PILOT
Exascale
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 826647
Notes: EPI Phase 1: EPAC RISC-V accelerators: Vector, ML/Stencil, Variable Precision, + shared cache coherent L2, and NoC. Shared Arm infrastructure
MEEP: FPGA emulation platform. ACME Accelerated Compute and Memory Engine: RISC-V accelerator w/ Vector processor + Video and neural network coprocessors.
eProcessor: 2-way OOO RISC-V processor, single core and dual core implementation (tapeout), coherent caches and off-chip coherent link, bioinformatics accelerator
EPI RISC-V Pilot: The European PILOT: Pilot using Local and Open Technologies: 2 All-European IP, independent PCIe 6.0 w/ CXL 3.0 accelerator chiplets, Vector and ML/Stencil (VEC and MLS). Open Compute Platform Infrastructure. Liquid Immersion cooling. Full RISC-V SW stack from GROMACS and EC-EARTH on the VEC side to Video Anomaly Detection, NLP and Machine Learning on the MLS side. Joint HPC +HPDA appt.

## Slide 29: eProcessor Stack
HPC
Applications
Middleware
AI
Applications
Middleware
Bioinformatics
Applications
Middleware
Fault Tolerance
Tools (compiler, performance monitoring, debugging)
Runtime (OpenMP, Tensorflow, Apache Spark, etc.)
Linux
2-way OOO Multicore + Adaptive caches and scratch pad
+ Bioinformatics Accelerator + Low Power
64,32,16-bit mixed precision
8, 4, 3, 2, 1-bit mixed precision

## Slide 30: eProcessor System diagram
Sys SW
HPC/HPDA SW
interconnect
LEGaTO PCB
Core
Core
Accel
Core
Core
Accel
Core
Core
Accel
Accel
Accel
Accel
(A)
(B)
CPU0
CPU1
Accel
Core
Core
Accel
CPU0
Coherent off-chip interface
Notes: 2-way OOO RISC-V core
Adaptive caches and scratch pad
Multi-core implementation
On-chip coprocessor interface
Bioinformatics accelerator
Coherent off-chip interface
Multi-socket implementation
COM Express PCB implement to leverage LEGaTO HPC infrastructure
Fault-tolerance
  Energy-efficient error detection and lossy checkpointing

## Slide 31: Rebuilding the European CPU Industry
EPI
MEEP
eProcessor
IP/Infra
IP/Infra
Design
Closed + Open
Open
Research
Production
eProcessor
EPI RISC-V PILOT
Exascale
IP/Infra
IP/Infra
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 826647
Notes: EPI Phase 1: EPAC RISC-V accelerators: Vector, ML/Stencil, Variable Precision, + shared cache coherent L2, and NoC. Shared Arm infrastructure
MEEP: FPGA emulation platform. ACME Accelerated Compute and Memory Engine: RISC-V accelerator w/ Vector processor + Video and neural network coprocessors.
eProcessor: 2-way OOO RISC-V processor, single core and dual core implementation (tapeout), coherent caches and off-chip coherent link, bioinformatics accelerator
EPI RISC-V Pilot: The European PILOT: Pilot using Local and Open Technologies: 2 All-European IP, independent PCIe 6.0 w/ CXL 3.0 accelerator chiplets, Vector and ML/Stencil (VEC and MLS). Open Compute Platform Infrastructure. Liquid Immersion cooling. Full RISC-V SW stack from GROMACS and EC-EARTH on the VEC side to Video Anomaly Detection, NLP and Machine Learning on the MLS side. Joint HPC +HPDA appt.

## Slide 32: The European PILOT
Stream 4: European PILOT
Stream 3: European RISC-V Accelerators
Stream 2: PILOT SW Stack
Toolchain:
System SW:
Runtime &
Schedulers:
AI Framework:
SW Libraries:
Applications:
GROMACS
EC-EARTH
Video
BERT
MD + AI
VEC Accel
ML/AI/Stencil
HPC Vector
Video
FFT
Neural Net
Tensorflow
BLIS
MPI
DLB
OpenMP
TAMPI
BeeGFS
SLURM
Boot, Drivers, Linux
Inference Engine
LLVM
Dace
Tarantella
VEC
MLS
+
Arm (Rhea, etc.) and/or x86 host
Accelerator Chassis
Accelerator PCB Cards
Accelerator Chips
Immersive Cooling
DROM
BBQUE
MLS Accel
oneDNN
MLS-DNN

## Slide 33: The European PILOT Accelerator Architecture
Accelerator Card
  3 C2C interfaces per chiplet, 8 lanes each
  1 PCIe 6.0 w/ CXL 3.0 interface per chiplet, 4 lanes
  4 x16 LPDDR controllers per chiplet
  Homogeneous or Heterogeneous PCB
  Optional FPGA/PCIe Switch
Accelerator Chiplet
Sea of Compute Tiles
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Compute
Tile
Common Uncore
IOTile
AXI
CHI
Serdes Phy
32Gbps
LPDDR Ctrl
AXI5
X16 Phy
LPDDR Ctrl
AXI5
X16 Phy
LPDDR Ctrl
AXI5
X16 Phy
LPDDR Ctrl
AXI5
X16 Phy
C2C Bridge
CHI
Serdes Phy
32Gbps
C2C Bridge
CHI
Serdes Phy
32Gbps
C2C Bridge
CHI
Serdes Phy
32Gbps
PCIe w/CXL
PCB
LPDDR4
x64
LPDDR4
x64
LPDDR4
x64
LPDDR4
x64
C0
FPGA or PCIe Switch
C1
C2
C3
33GB/s
33GB/s
33GB/s
33GB/s
VEC
MLS
ALL
Compute
Tiles
OR

## Slide 34: Rebuilding the European CPU Industry
EPI
MEEP
eProcessor
IP/Infra
IP/Infra
Design
Closed + Open
Open
Research
Production
eProcessor
EPI RISC-V PILOT
Exascale
IP/Infra
IP/Infra
The MEEP project has received funding from the European High-Performance Computing Joint Undertaking Joint Undertaking (JU) under grant agreement No 946002. The JU receives support from the European Union’s Horizon 2020 research and innovation programme and Spain, Croatia, Turkey.
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 826647
Notes: EPI Phase 1: EPAC RISC-V accelerators: Vector, ML/Stencil, Variable Precision, + shared cache coherent L2, and NoC. Shared Arm infrastructure
MEEP: FPGA emulation platform. ACME Accelerated Compute and Memory Engine: RISC-V accelerator w/ Vector processor + Video and neural network coprocessors.
eProcessor: 2-way OOO RISC-V processor, single core and dual core implementation (tapeout), coherent caches and off-chip coherent link, bioinformatics accelerator
EPI RISC-V Pilot: The European PILOT: Pilot using Local and Open Technologies: 2 All-European IP, independent PCIe 6.0 w/ CXL 3.0 accelerator chiplets, Vector and ML/Stencil (VEC and MLS). Open Compute Platform Infrastructure. Liquid Immersion cooling. Full RISC-V SW stack from GROMACS and EC-EARTH on the VEC side to Video Anomaly Detection, NLP and Machine Learning on the MLS side. Joint HPC +HPDA appt.

## Slide 35: The Future: Flagship RISC-V Exascale Accelerator
Open Source HW
MEEP
Open Source SW
Exploitation
European Open Source Ecosystem
Arm GPP EuroHPC-2020-01 subtopic A
RISC-V Accelerators
RISC-V CPUs
eProcessor
EPI - SGA2
Note: Collaboration between all RISC-V projects possible
Flagship Accelerator Program (RISC-V)
The European PILOT (RISC-V)
Flagship CPU Program (RISC-V)
EPI - SGA1
Notes: 5 year flagship accelerator project
7 year flagship CPU project

## Slide 36: A Successful EC Roadmap for the Future
Embrace Open Source Hardware
  Build infrastructure to support open source
  Create an environment that links research to the ICT industry
  Supported by DG Connect and DG IT
Teach, train, and collaborate
Leverage the Global Technology ecosystem
Requires SIGNIFICANT funding for programs to build made in Europe IP
  Many focused projects: Horizon Europe, Digital Europe, …
  Many focused teams: Collaborative IP and TRL development
  Total and integrated vision for the future
  Large Accelerator and CPU investment (> 1B€)

## Slide 37: The Future is Wide Open!
There is an urgent need, from mobile phones to supercomputers: more compute at lower power
Our main goal: Create European chips that meet the needs of future European and global markets across HPC, cloud, automotive, mobile to IoT
This is the framework for the Exascale Supercomputing Initiative at BSC
An opportunity for Europe to lead the charge to creating a full stack solution for everything, from supercomputers down to IoT devices
The RISC-V ecosystem is in the nascent period where it can become the de facto open hardware platform of the future

## Slide 38: LOCA @ BSC

## Slide 39: BSC full stack
Hardware
HPC Applications
Software/Hardware
Co-Design
SW
HW
Missing Hardware Design
& Implementation Piece
HPC Hardware
Specialization using
HW/SW Co-Design

## Slide 40: LOCA Goals
Mechanism to extend open source ecosystem to include H/W
  Add H/W expertise to BSC and European partners, leverage existing S/W expertise
  Provide proven/usable Open Source H/W
  Intersection of academia and industry
  Open European IP repository → rapid implementation
  Catalyst to reinvigorate European ICT industry
  Global collaboration and training center
  Incubator for European IP

## Slide 41: European Collaboration & Education
Traditional chip design is done in a Master/Apprentice environment
LOCA recreates this environment by bringing in Masters from industry to collaborate with a variety of people, pushing beyond RTL
Professors, students, and industry veterans all together
Ideal sandbox for creative and innovative work
Research and Design to chip fabrication
Casteller
(human tower)

## Slide 42: LOCA is Bigger than Barcelona!
Casteller
(human tower)
European
Open Hardware,
Architecture
Initiative
We must stand on the shoulders of giants to build great things. We are assembling many giants and hope you can join us.

## Slide 43: Thank you
mateo.valero@bsc.es